## Slide 1: Combined, High Resolution Bathymetric and Shoreline Survey Solutions for Dredging and Construction Operations
WEDA Midwest Chapter Conference
April 27, 2012
Kyle Enright

## Slide 2: Data Collection Methods
Single beam
  Data under head (beam width dependent)
Single Beam Sweep
  Multiple transducers (beam width dependent)
Notes: Single beam echosounder is an easier and cheaper setup. Dredgers best friend as it would be futile to achieve full bottom coverage as this system is limited to its first sonic return within its sonic cone (degree specified i.e. 3 degree beam). Without RTK GPS quality tide solution vessel would require squat and settlement calculations and depth and position become questionable.
Single beam sweep with the addition of more single beam echosounders one can increase your coverage. With the right degree beam you could achieve full bottom coverage of the first return (highest point) within the sonic cone. Motion unit recommended as uncorrected roll values can result in false or misleading bottom returns.

## Slide 3: Data Collection Methods – cont.
Multibeam
  Number of beams, error/swath coverage, beam degree
Dual Head Multibeam
  Rotation, number of beams, overlap, calibration
Notes: Multibeam functions in a similar way to the sweep, just that the beams transmit from one unit rather than multiple units along a pole. Multibeams can offer hundreds of sounding in a single ping and can cover around 3 times water depth (depending on the unit). Beam degree can be inversely beneficial as single beam and sweep. Smaller degree beams produce higher precision especially when combined with a higher number of beams.
Dual Head Multibeam. Adding a second multibeam head and rotating them both outward from each other can increase coverage and number of sounding per ping (doubles) (but halves ping rate on some systems). It is inevitable that the heads will have overlaping soundings/data and help for quality control procedures. However having two heads that are rotated makes it more complicated to perform a system calibration based on measurements from vessel origin and pitch, roll and yaw values.

## Slide 4: Data Collection Methods – cont.
Vessel-mounted LiDAR
  Scans per second, calibration, lever-arm to motion unit, integration of laser scanning and photogrammetry, position QC
Notes: VML is not overly common, but it beginning to become more prevalent in construction and survey industries. This can be treated similar to a multibeam above water. Its scans per second compares to ping rate and calibration and relation to origin are all treated in a similar fashion. Newer lasers can have photographic data imbedded into the data points which actually colors the data point and creates an extremely realistic 3-D data set. The position QC can be more challenging as it is derived in post processing rather than an instantaneous check.

## Slide 5: Single Beam Sweep
Efficient mapping in 0.5 to 15 feet of water (wider coverage with longer booms)
Can be configured for wider swath depending on required detection resolution and coverage requirements
Typical Tetra Tech sweep: 6 transducers, 25-foot swath
USACE routinely utilizes single beam sweep for river navigation channels
Notes: Swath dependent on boom width. As you can image this has diminishing returns as the pole can be caught on many many things. We have found that this system is better for shallow waters and can provide more coverage than multibeam in waters 6ft or less.
multibeam and sweep can easily be used on the same job in the same area…better with two boats. But the slide shows an example of a data set were the river has a distinct channel that is easily surveyed with MBE and shallow areas that are better collected with a Sweep system. By using similar RTK GPS, motion units and qc methods it is not surprise to see the data complement each other within small factions of a foot.

## Slide 6: Single Beam Sweep Data
Notes: Data example of a large shallow area surveyed in a skunk striping method with a sweep system. You can see the only real limitation is the lack of complete coverage. The benefit of using the sweep over a single single beam would be dramatic increase in collection efficiency and coverage, outer poles can reach in shorelines easier without losing GPS coverage under trees etc.

## Slide 7: Dual Rotated Multibeam Echosounder
Each system rotated 30 degrees
Data collection under structures, up bank to water surface (180° swath)
Orientation increases coverage and efficiency in channelized areas
Survey of either bank, up or down river or shoreline

## Slide 8: Multibeam Sonar Data Examples
Notes: High resolution structural scans
Forebay
Intake structures
Trash racks
locks

## Slide 9
  120-ft
  40-ft
  120-ft
2009
2011
2009 (green) / 2011 (yellow)
Bi-annual Comparison
Notes: Sand wave structure, bottom elevation and sediment transport vary by flow conditions.

## Slide 10: Multibeam vs. Single Beam
Notes: Similar, but lacking of detail and true deep and shoals. (hard to see I am sure…good pyschological trick to make the MBE data prettier and easier to understand)
Sunken boat filled with spiny lobsters (sent divers down) found amongst many other definitive features.

## Slide 11: Navigational Survey
Ferry crossing on a high flow river
Ferry required repairs after striking 2 m wide rock sticking up 0.7 m higher than surrounding shoal
Identify other possible routes until bridge construction finishes

## Slide 12: Vessel-mounted LiDAR
Maps river bank and structures with full coverage
Resolution similar to multibeam plus photos/video
Efficient survey in >1-ft water depths
Continuous terrain model of river bank, bottom and under structures with multibeam and/or multi-channel (260° swath)

## Slide 13: Vessel-mounted LiDAR
Riegel LMS-Q120 Laser scanner and digital cameras
LiDAR point cloud data
100% coverage with bathymetric and aerial LiDAR data

## Slide 14: Combined Vessel-mounted LiDAR and Multibeam
Cross section cut through VML and MBE data showing excellent correlation. VML data in purple MBE data in green. Note 5x vertical exaggeration.
Similar systems integration enables acceptable repeatability across sonar and laser scanning systems.

## Slide 15: Combined Vessel-mounted LiDAR and Multibeam
Notes: There is a noticeable line between VML and MBE, there was little to no change in water levels, so no overlap was collected.

## Slide 16: As-built Model from Combined Data Set
Notes: You can see the tower from the previous slide.
This is an excellent example of how the survey data can turn into a working 3 D model of this dam structure.
There also was a CAD drawing created of the intake house, both serve was excellent as-builts for this structure.
the combined dataset was used both for as built model (all be it a 100 years old) and for design of new intake and fish bypass structures.
Data was also used to locate and avoid submerged trees as netting and equipment was brought in for the fish by-pass

## Slide 17: Photo-integrated 3D Laser Scanner Data
Notes: This collected data was presented to the client using Leica’s Tru-view an FREE interactive plug-in which works within Internet Explorer.
Truview advantage:
Truview drapes a 360 degree image over top of all of the scanning point.
Typical scanner viewing software only allows the user to look around.

## Slide 18: The END….questions?